## Slide 1: Energy crops’ Phytotechnology with Biomass production at the marginal and contaminated lands
Prof. Valentyna Pidlisniuk, UJEP, Czech Republic

## Slide 2: Content of Presentation
Fundamentals of phytoremediation & phytomanagement
Energy Plants in Phytoremediation
Phytoremediation parameters
Miscanthus as a perspective phytoagent
Miscanthus tolerance to TEs: Lab research
Phytomanagement with Miscanthus supported by different agricultural practices:
role of PGRs
role of isolates
role of amendments

## Slide 3: Definition of Phytoremediation
Phytoremediation technology was established as an environment-friendly concept to restore polluted sites before 1990, and a year later the term was used.
The term phytotechnologies, which replaces the earlier term phytoremediation, is also known as green-remediation, and in general, means using plants to degrade, extract, contain, transform into less harmful forms, or immobilize contaminants in soil, water, or air with inorganic or organic compounds.

## Slide 4
Phytoremediation
Bioremediation
Physico-chemical
remediations
Dig & dump
Cost
Environmental friendliness
Social acceptability
Time
Interest of phytoremediation
Notes: 4
4

## Slide 5: Phytoremediation Mechanisms Depending on the Contaminants
At sites contaminated with inorganic compounds: TEs, plants stabilize or remove contaminants by three mechanisms:
Phytostabilization, where plant roots immobilize contaminants in the soil thereby decreasing soil and wind erosion of contaminants
Rhizofiltration, where plants adsorb contaminants onto the roots
Phytoextraction, where plant roots absorb contaminants into the aboveground plant parts (i.e. leaves, branches, and/or stems).
At sites contaminated with organic compounds plants break down or remove contaminants by three mechanisms:
Phytodegradation, after the plant absorbs the organic contaminant, plant enzymes breakdown the contaminant to safer compounds
Rhizodegradation, where plant roots provide the beneficial environment for microbes that in turn break down organic contaminants in the root zone
Phytovolitalization where plants take up contaminants and release a safer, mediated form of the organic compound into the atmosphere
Rhizodegradation

## Slide 6: Phytoremediation versus Phytomanagement
Phytoremediation is the process of using plants and grasses to remediate the contaminated soil/wetlands.
Plants used for phytoremediation:
  have to be stressful to contaminants, pests and diseases,
  have to be able to grow at the same land during years and produce biomass.
The broader concept of phytomanagement is new and includes economic benefits.
Phytomanagement: use of plants to reduce and control risks arising from soil pollution while contemporaneously making a profitable and sustainable use of the resource by producing marketable biomass" (Evangelou et al., 2015).

## Slide 7: Plant in Phytoremediation
Plants used for phytostabilization should be able to grow well in the contaminated soil, produce a product of value and commercial interest, and evapotranspire sufficient water to achieve containment of the contaminants.
Plants used for phytoremediation have to be stressful to contaminants, pests and diseases.
Based on the relative uptake and bioaccumulation potential, plants can be grouped into three main categories: excluder, indicator, or accumulator
Hunt et al, 2014

## Slide 8
Excluders are tolerant to high elements concentrations and their tolerance is achieved by preventing the absorption and translocation of toxic elements to above ground biomass. These species have low potential for elements extraction, are insensitive to elements over a wide range of concentrations, and a common example is various grass species.
Indicators are plant species sensitive to elements and consequently certain symptoms can be manifested. Such plants are not tolerant to high concentrations of trace elements, and examples are grain and cereal crops.
Accumulators are plants which accumulate trace elements in various concentrations, however, in concentrations which are still lower than in case of hyperaccumulators; example- indian mustard, cabbage.
Hyperaccumulation is a specific characteristic inherent in certain species. For successful hyperaccumulation the concentrations of the elements in the above-ground biomass have to be extremely higher compared to their content in the soil;example- dandelion,mustard. The majority of hyperaccumulators are endemic plants which grow in soils rich in trace elements and behave like strict metallophytes. These plants have developed special mechanisms for element uptake and tolerance to high concentrations. The negative aspect of hyperaccumulators is low biomass yield.

## Slide 9
The ability of plants to accumulate elements from the soil can be estimated by:
Enrichment Coefficient (EC) or the Bioconcentration factor (BCF), which are expressed as the ratio of defined element concentrations in the plant material (mg kg-1 of dry matter) and in the soil (mg kg-1 of dry soil). According to EC plants are defined as:
high accumulator plants EC 1 – 10
medium accumulator plants EC 0.1 – 1
low accumulator plants EC 0.01 – 0.1
non accumulator plants EC < 0.01
Translocation factor (TLF) value reflects the levels of plants phytoextraction potential accounting as a ratio of the contaminants’ concentrations in the aboveground biomass to their concentration in roots.
Phytoremediation parameters

## Slide 10
Biofuel crops for biotechnology
Second generation biofuel crops represent not-food crops and are less directly in conflict with food crops
Crops for second generation biofuels can be divided into two main categories:
short rotation
canopy species
Willow
( Salix
spp.)
Poplar
( Populus spp.)
Locust
( Robinia
spp.)
perennial/
annual grasses
Reed canary
grass
Phalaris
arundinacea L.
Miscanthus (Miscanthus sinensis A.., Miscanthus sacchariflorus M., Misccanthus x giganteus)
Switchgrass
(Panicum
virgatum L.)

## Slide 11: Miscanthus × giganteus Greef et Deu (giant miscanthus)
Giant miscanthus is C4 photosynthesis with high water and nutrient-use efficiency plant that belongs to the Poaceae family and originates in Eastern Asia (China). It is a hybrid of Miscanthus sinensis, native to China, and M. sacchariflorus, native to Japan.
Necessary climatic conditions:
tolerant to cold (up to -6℃);
tolerant to drought;
at least 150-300 mm annual precipitation;
Height: more than 4 m.
Preferred soil type: well drained soils (pH 5.5-7.5).
Annual yield: 10-45 t of DM ha-1.

## Slide 12: Miscanthus as Phytoagent*
M. x Giganteus is an ideal plant for phytoremediation:
Crop can be produced at the same land for about 20 years
Crop constantly and annually produces biomass
Crop is stable to different stress factors like contaminants in the soil and diseases
Crop does not require a lot of minerals during growing, indeed it enriched soil with nutrients, C and humus
Crop has a unique ability to give sufficient yield with low input and uptake of contaminants
Excellent candidate for growing on marginal and deteriorated land, slightly contaminated land
Phytomanagement with Miscanthus: includes economic benefits from the biomass ( alternative energy sources, bioproducts- fibers, isolation materials, pulp and paper)
* Pidlisnyuk V., Stefanovska T., Lewis E., Erickson L., Davis L., 2014. Miscanthus as a productive biofuel crop for phytoremediation. Critical Review in Plant Science, 1: 1-19

## Slide 13
Miscanthus yield at the research fields in the Czech Republic*
clones of Miscanthus × giganteus reached average biomass yields in between 10-15 t DM ha (13 years)
despite very dry and warm periods and low-input agrotechnology = adaptation to climate change in lowlands (Michovky)
M.xgiganteus has a good potential to become important biomass crops for future bioenergy and bio economy
Chart: Precipitation (mm)
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Precipitation (mm) Michovky | 517 | 502 | 599 | 764 | 563 | 553 | 667 | 548 | 427 | 499 | 533 | 354 | 521
Precipitation (mm) Lukavec | 777 | 604 | 788 | 940 | 670 | 724 | 876 | 707 | 576 | 601 | 777 | 509 | 680
temperature ( C) Michovky | 10.2 | 9.8 | 9.4 | 8 | 9.6 | 9.5 | 9 | 10.6 | 10.7 | 10 | 10 | 11 | 10.7
temperature ( C) Lukavec | 8.5 | 8.6 | 8.4 | 7.2 | 8.4 | 8.1 | 7.3 | 8.6 | 8.7 | 7.9 | 7.9 | 8.8 | 9.1
Chart: Yield ( t DM/ha/y)
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
M x gigantheus Michovka | 1.7615 | 11.4059 | 18.7223 | 19.9122 | 16.1723 | 16.8969 | 16.6192 | 15.2231 | 19.5556 | 16.0654 | 15.7762 | 15.1363
M sinensis Michovky | 2.054 | 9.1637 | 9.5173 | 12.3001 | 11.0573 | 10.3058 | 10.0004 | 10.3883 | 11.4017 | 11.8972 | 10.0142 | 10.8569
M x gigantheus Lukavec | 1.3359 | 9.8534 | 12.6897 | 18.7914 | 14.017 | 15.5718 | 11.3033 | 8.5354 | 11.7804 | 12.426 | 8.7852 | 12.7272
M sinensis Lukavec | 1.8868 | 8.9067 | 11.3976 | 13.4654 | 12.7683 | 10.3432 | 8.3774 | 7.3229 | 8.1192 | 10.2342 | 8.8398 | 10.1664
Weger et al, 2020
Notes: 13
13
13

## Slide 14
Advantages and disadvantages of Miscanthus for phytotechnology
with biomass production *
Advantages | Disadvantages
In production | 
Perennial, established stands last ~20 years | Takes 2-3 years to fully establish
Effectively suppresses weeds once established | Tall, dense growing perennial grass monoculture with limited wildlife friendly uses
High productivity of biomass compared to other energy crops (20 up to 35 tons.ha-1.yr-1) | Bioenergy processing immature technology; expensive pre-processing needed
Uses water efficiently by C-4 photosynthesis; total usage ~ 1 m.yr-1 | Yields are influenced by water availability; under low-rainfall conditions may be poor
Grows at lower temperatures than other warm season (C-4) grasses; hence longer season | Limited tolerance of low winter temperatures so not suited to severe continental climates
Does not require as much N as sorghum, maize, oil palm, or sugar beets | Off-take of K ~3 x more than coppice willow
Mineral content of biomass relatively low compared to common biomass crops | Mineral nutrient content per unit energy high compared to coal
The winter harvested crop is relatively dry, so drying costs are low | Field drying and mineral leaching results in significant biomass loss as leaf fall
* Pidlisnyuk et al, Critical Review in Plant Science, 2014 ,N1, p.1-19

## Slide 15
In phytoremediation | 
Economic return can be obtained from contaminated land with employment and market value of biomass fuels (possibility of developing a more economical approach to remediation of soils with heavy metals such as mine land) | Dedicated energy crops can result in displacement of other crops with significant changes in land use, food crop prices
Easier to clear than trees for the site to be transformed for future use | Sterile hybrid so propagation for initial establishment is labor intensive
In both processes | 
Potential for income generation through carbon credits through CO2 sequestration | Less C storage than forest wood crops over next 50 years
Reduction of soil erosion due to rainfall, or wind. Reduces dust | Can serve as reservoir for insect pests of other species
Advantages and disadvantages of Miscanthus for phytotechnology
with biomass production*
* Pidlisnyuk et al, Critical Review in Plant Science, 2014, 1, p.1-19

## Slide 16
Miscanthus tolerance of TEs and salts
Slovakia, Sliac soil,2014
Many published lab studies, some with soils having aged contamination show low accumulation ratios for As, Pb, Cd, Zn
Few field studies done on heavily contaminated soils.
Aged contamination with > 500 mg/kg Pb in Poland showed little uptake.
A smelter site in France showed accumulation ratio <0.1 with tissue Pb ~ 15 mg/kg from soils of 200-500 mg/kg Pb. This agrees well with our work (See following slides).
In Romania a mining area site with > 600 mg/kg Pb showed only 10 mg/kg in leaves. Cd levels likewise were low, about 1 mg/kg from soil with 13. However stem Cd was higher by 2x while stem Pb was lower by 2x relative to leaves. Rhizomes had high levels, about half of soil values.

## Slide 17: Case 1. Metals contaminated military soils from Sliac, Slovakia and Kamenetz, Ukraine
Kamenetz, year 1
Sliač, year 1
Sliač, year 2
Kamenetz, year 2
*Pidlisnyuk V., Erickson L., Stefanovska T., Popelka J., Hettiarachchi H., Davis L., Trogl J., 2019. Potential phytomanagement of military polluted sites and biomass production using biofuel crop Miscanthus x giganteus. Environmental Pollution, 249, 330-337
PCA1 (90.21%)
PCA1 (89.94%)
PCA1 (52.71%)
PCA1 (92.09%)
Good growing during two vegetation, ensuring application of Mx.giganteus to the military sites
In year 1:
the figures reflect the elements take up into all parts of Miscanthus with the highest value in roots ( phytostabilization)
In year 2:
relative uptake to the stems and leaves decreased tremendously – distributions for stems and leaves are far smaller and located in the almost same positions in the PCA biplot.
Miscanthus Tolerance to TEs

## Slide 18: Case 2. Metals contaminated post-industrial soil from Bakar, Croatia*
Point source polluters in Rijeka-Bakar area, Croatia
.
Miscanthus Tolerance to Trace Elements
*Pidlisnyuk V., Shapoval P.,Zgorelec Z., Stefanovska T., Zhukov O., 2020. Multiyear phytoremediation and dynamic of foliar metal(loids concentration during application of Miscanthusxgiganteus Greef et Deu to polluted soil from Bakar, Croatia. Environmental Science and Pollution Research, 27: 31446-31457.
Results showed the proper development during three years in the highly metals polluted soil with sufficient biomass production
Year Harvested day Seria Contamination level
clean 75%/25% 50%/50% 25%/75% 100% contaminated
2015 November, 21 A 132.77 80.36 55.65 48.65 50.76
B 147.23 76.92 52.32 45.93 42.62
2016 December, 22 A 129.95 78.65 47.81 54.85 45.58
B 148.45 69.92 50.60 44.77 42.87
2017 December, 16 A 125.51 74.09 40.82 57.84 41.62
B 145.02 67.59 46.75 41.06 39.59
Miscanthus biomass (g/treatment)

## Slide 19: Case 3. TEs contaminated mining soil, Tekeli, Kazakhstan*
The mining soil belongs to Tekeli Mining and Processing Complex of "Kazzinc”. Soil contaminations: Pb exceeded limited level in 29 times, As –in 5 times, Zn – in 11 times, Sr - in 22 times, Cu - in 13 times. Soil is saline, sandy, pH of aqueous extract was 8.27-9.89.
M. × giganteus was stress-tolerant and growth well two vegetation. Monitoring of 11 elements (As, Pb, Zn, Co, Ni, Cr, Cu, Sr, Mn, V, U) in the plant tissues (root, stem and leaves) and soils showed that the greatest content of elements was accumulated in the roots.
M.×giganteus works as an excluder (BСF, TF <1) and accumulated monitored elements (As, Pb, Co, Ni, Cr, Cu, V, U) preferably in the roots.
In the case of Mn, Sr and Zn showed an ability to phytoextraction (BСF <1 and TF ≥ 1)
Miscanthus Tolerance to Trace Elements
*Nurzhanova A., Pidlisnyuk V., Abit K., Nurzhanov Ch., Kenessov B., Stefanovska T., Erickson L.., 2019. Comparative assessment of using Miscanthusxgiganteus for remediation of soils contaminated by heavy metals: a case of military and mining sites. Environmental Science and Pollution Research, 26: 13320-13333.

## Slide 20: Case 5. TEs contaminated abandoning mining soil, Pokrov, Ukraine*
The post mining soil was consisted of the mixture of loess-like loam and red-brown
clay passed through a long-term melioration stage.
Application of amendments (to the post-mining land (positively affected the growth parameters of M.xgiganteus: increasing of plant productivity from 50 to 140%.
Application of amendments permitted to obtain the similar Miscanthus yields as at the arable lands
Evaluation the impact of soil amendments added to soil once before the vegetation to biomass production:
a) mineral fertilizer with a balance of nutrients N60:P60:K60 kg.ha-1;
b) mixture of ash and sewage sludge (10 t.ha-1);
c) double dose of sludge (20 t.ha-1).
Miscanthus Tolerance to Trace Elements
*Kharitonov M., Pidlisnyuk V., ,Stefanovska T., Babenko M., Martynova N,, Rula I., 2019. The edstimation of Miscanthusxgiganteus\ adaptive potential for cultivation on the mining and post0mining lands in Ukraine . Environmental Science and Pollution Research, 26:2974-2986

## Slide 21: Utilization of different agricultural practices: Miscanthus promoting bacteria
Všebořice dump – former open-case brown mine
GPS: 50°42'11.9"N 13°58'32.1"E

## Slide 22: Plant Growth Promotion Bacteria*
*Pranaw K., Pidlisnyuk V., Trögl J., Malinská H.: Bioprospecting of a novel plant growth-promoting bacterium Bacillus Altitudinis KP-14 for enhancing Miscanthus × Giganteus growth in metals contaminated soil. Biology 9(9) (2020) 305. DOI: 10.3390/biology9090305
Isolate | P-Solubilization (in µg/mL) | IAA (in µg/mL) | ACC | Ammonia | Siderophore | HCN | Antifungal activity | 
 |  |  |  |  |  |  | Fusarium culmorum (CCF-1745) | Botrytis cinerea (CCF-2361)
KP-14 | 130.0±3.2 | 27.8±0.8 | + | + | + | + | + | +
KP-18 | 14.5±2.9 | 10.5±0.2 | - | + | + | + | + | -
KP-19 | 32.8±1.2 | 1.1±0.7 | - | + | + | - | - | -
Chart: Weight (in g)
| Leaves | Stems | Roots
Uninoculated (control) | 10.995 | 9.205 | 27.135
Inoculated (treatment) | 16.3675 | 17.105 | 42.21
The inoculation of M. × giganteus rhizomes by the PGPB B. altitudinis strain KP-14 significantly enhanced plants’ bio-parameters : biomass of leaves increased by 23%; stems- by 86% and roots by 76%.
The tolerance profile and PGP properties of Bacillus altitudinis strain KP-14

## Slide 23
Thanks to the members of NATO G4687 team
Lawrence Davis1A , Larry E. Erickson 1B, Ganga Hettiachchi1C, Tetyana Stefanovska2 , Josef Trogl3 Asil Nurzhanova4, Pavlo Shapoval5
1 Depts of: A; Biochemistry, B; Chemical Engineering, C; Agronomy, Kansas State University, Manhattan, KS
2 National University of Life and Environmental Science, Kyiv, Ukraine
3 Jan Evangelista Purkyne University, Usti nad Labem, Czech Republic
4 Institute of Plant Biology and Biotechnology, Almatu, Kazakhstan
5 National University Lvivska Polytechnika, Lviv, Ukraine
Support for this research came principally from a NATO SPS MYP G4687
Also some part of research is supported by:
Center for Hazardous Substance Research at K-State, USA;
Czech Technical Agency, Czech Republic
Kazakh Ministry of Education and Science, Republic of Kazakhstan
Maize
Sorghum
Thanks to the members of CORNET MiscanValue team
Crop Research Institute: Sergey Ust’ak, Jakub Munoz
UJEP: Ethan Duong, HTW-Dresden,Josef Trogl, Aigerim Mamirova
WASTen: Radek Horenovsky and Vojtěch Brož,
Germany: TUD HFT: Daniela Einer and Soren Tech; TUD AST: Siegfried Firus and Mirko Lindner; PTS: Martin Zahel and Manuela Fiedler
en
Miscanthus biomass
Czech Republic
“Creating value chains for utilization of miscanthus fibres from sustainably managed marginal and post-mining areas“
Young researchers:
Martin Sozansky, Vytalyi Stadnik (NULP, Ukraine),
Masha Obruch, Artem Medkov (NULES, Ukraine)
Diana Nebeska (UJEP, Czech Republic)
Zafer Alasmari (KSU, USA)
Miscanthus bioproducts
Germany

## Slide 24
www.military-site-cleaning.cz
https://miscanvalue.wasten.cz
Questions?