## Slide 1: CZ.02.2.69/0.0/0.0/16_015/0002408 Univerzita 21. století – Kvalitní, moderní a otevřená instituce KA07 Poradenské centrum UJEP, Prevence studijní neúspěšnosti
Biofuels and bioenergy crops
Josef Trögl, Valentina Pidlisnyuk, Diana Nebeská, Hana Malinská

## Slide 2: Outline
  Motivation and introduction
  Overview of biofuels
  Fuels from wastes
  Research Miscanthus x giganteus on marginal lands

## Slide 3: Motivational introduction – why biofuels?
Chart: 
| Solid Fuels | Petroleum and Products | Renewables | Gases | Nuclear
EU | 0.14821 | 0.34919 | 0.13337 | 0.2358 | 0.13342
Chart: 
| Solid Fuels | Petroleum and Products | Renewables | Gases | Nuclear
CZ | 0.39148 | 0.19471 | 0.10154 | 0.16529 | 0.14698
Chart: 
| Solid Fuels | Petroleum and Products | Renewables | Gases | Nuclear
Iran | 0 | 0.55 | 0.028 | 0.42 | 0.002

## Slide 4: Motivational introduction – why biofuels?
 | Iran | EU | Czechia
Crude oil production 2016 [Mtoe] | 216 | 60 | 0.19
Trade [Mtoe] | +122,6 | -550 | -7.7

## Slide 5: EU – Oil production

## Slide 6: EU – oil import

## Slide 7: EU – oil usage
Chart: 
| Plastics 4-6% | Other 7-9% | Energy 42% | Transport 45%
 | 5 | 8 | 42 | 45

## Slide 8: Why biofuels?
Energetic security
  EU energetic demands are dependent on petroleum and natural gas, but the production is very low
Environmental and climate protection
  low carbon economics
Economic and societal impacts
  development of rural areas
  new jobs
  impulses for innovation

## Slide 9: Renewable energy EU policy
  EU set a climate and energy targets to be met in 2020, known as 20-20-20 targets:
    reduction in EU GHG emissions of at least 20% below 1990 levels
    20% reduction in primary energy use compare with projected levels
    20% share of energy from renewable sources by 2020 (Directive 2009/28/EC on renewable energy)
    of which 10% share of renewable energy specifically in the transport sector

## Slide 10: Biofuels in EU strategies
  The EU sets out 7 strategic policy areas:
    stimulate demand for biofuels
    ensuring environmental benefits
    developing the production and distribution of biofuels
    expand feedstock supplies
    enhance the trade opportunities of biofuels
    support developing countries
    support research and innovation

## Slide 11: EU directives
  2003/30/EC – The first biofuels directive
    goals
    obligatory addition of biofuels into petroleum fuels
  2009/28/EC – Reconsidering goals not to be damaging
    ban of the first generation for new productions
    adopting sustainable indicators
  revision in 2015

## Slide 12: Definitions
  “Biomass means the biodegradable fraction of products, waste and residues from agriculture (including vegetal and animal substances) forestry and related industries, as well as the biodegradable fraction of industrial and municipal waste”
  “Biofuel means liquid or gaseous fuel for transport produced from biomass”
  Directive 2009/28/EC

## Slide 13: Biodiesel
Substitute of diesel
Methyl (ethyle) esters of natural fats
Produced by transesterification
H
2
C
H
C
H
2
C
O
O
O
C
C
C
O
O
O
CH3OH, NaOH
H
3
C
H
C
H
3
C
O
O
O
C
C
C
O
O
O
3
H
2
C
H
C
H
2
C
OH
OH
OH
+
+
+

## Slide 14: Biodiesel
  Advantages:
    Can replace standard diesel in any ration
    Does not contain petroleum admixtures – PAHs, S …
  Disadvantages
    Susceptible to hydrolysis  free fatty acids have corrosive effects
    Lower octane number than petroleum diesels

## Slide 15: Bioethanol
  Substitute of gasoline
  Produced by ethanole fermentation from sugars
    Probably the oldest and most profitable biotechnology process in the world
  Advantages
    High octane number – can replace other anti-knocking admixtures such as MTBE or tetraethyl-Pb
    Does not contain admixtures from petroleum, e.g. PAHs, S…
    Majority of car engines can take it up to 20%
  Disadvantages
    Lower logPO/W  can affect plastic / rubber pieces
    Can contain traces of water  corrosion
    Lower energy  higher car consumption

## Slide 16: Hydrogen
  Produced by some cyanobacteria during photosynthesis
  Produced by some fermenting bacteria (Clostridia) but in mixtures
  Advantages
    Very clean – even no CO2
    High energy
  Disadvantages
    Problematic storage
    Potentially hazardeous
    Requires different engines

## Slide 17: Biobutanole
  Produced by some Clostridium acetobutylicum
  ABE process (acetone – butanole – ethanole fermentation)
  Can be used alone or as a source for further syntheses

## Slide 18: Biogas
  Substitute of natural gas
  Produced by anaerobic digestion of biomass
  Advantages
    Lot of biomass including wastes (from food, wastewaster-sludges…) can be used
  Disadvantages
    always mixture of CH4+CO2  lower energy or complicated separation

## Slide 19: Generations
  „0 generation“ - Biomass for heating and electricity production
    wood, straw
  1st generation biofuels – biodiesel, bioethanol and biogas from intensively cultivated food crops
    palm oil, rape, sunflower, soy, wheat…
  2nd generation – biofuels from lignocellulotic crops, extensivelly growing
    fast growing trees, perenial grasses
  3rd generation – biofuels from autotrophic microorganisms (algae)
  4th generation – biofuels from genetically engineered organisms / bio-photo fuel cells

## Slide 20
First generation BIOFUELS
First-generation biofuels use
- sugar and starch crops (bioethanol - ETBE):
- maize
- sugar beet
-sugar cane
- oilseed crops (biodiesel – FAME – MERO):
- rapeseed
- sunflower
- soybeans
-oil palm
As feedstock compete directly with demand for these crops as food or feed

## Slide 21
First generation BIOFUELS
Advantages
Advantages (direct and indirect):
- displacing fossil fuels
- surplus production of food crops in industrialized countries can be
effectively utilised
- utilisation of marginal lands
- increase employment in rural areas ( from harvesting and processing,
connected with construction of new biofuel-producing facilities)

## Slide 22
First generation BIOFUELS
risks
Soil and land
- land-use changes:
- expanding the amount of land under cultivation for energy is the reversible conversion of virgin ecosystems
- intensification, increased pollution load and biodiversity loss
- intensification of land-use:
- cause soil fatigue
- decreasing of the nutrient and organic matters
- increasing in pests and than increasing in fertilisers (acidification, eutrophication)
- pesticides application
- soil compaction

## Slide 23
First generation BIOFUELS
risks
Water
- irrigation  the shortages of water resources
- run-off of agro-chemicals and other waste products can pollute nearby
waterways, threatening wildlife and speeding eutrophication
Air
- air quality is affected from farm machinery (which runs mainly on diesel and cause air pollution during planting and harvesting)
Biota
- GM crops expansion
- decreasing of areas of natural ecosystems
- threats to biota from agricultural chemicals

## Slide 24
First generation BIOFUELS
risks
Risks (direct and indirect):
- limited potential to provide sustainable fuels
- compete to food and feed production and cause increase in food prices
(e.g. rapeseed oil) and to threaten food safety what is caused by free
global market and movement of goods and capital
- nowadays food safety is in Germany 94%, Poland 85%, Czech Republic 72%,
Slovakia 50%;
- in 1990 food safety in Slovakia was 80%,for some commodities it was 100%
- 30% decreasing during 20 years period; it is the biggest one across the EU

## Slide 25
Second generation BIOFUELS
Second-generation biofuels (not yet widely available commercially) use biomass from non-food sources, including
- lignocellulosic biomass:
- grasses from permanent grasslands
- grass is composed of :
20-30% cellulose
15-25% hemicellulose
3-10% lignin
- waste matter from food crops or residues from other non-food processes:
- harvest residues from cereals
- corn stover composed of:
35% of cellulose
28% hemicellulose
16-21% lignin

## Slide 26
Second generation biofuel crops which represented by not-food crops are less directly in conflict with food crops and would not effect the price of food
Crops for second generation biofuel production can be divided into two main categories:
short rotation
canopy species
Willow
( Salix
spp.)
Poplar
( Populus spp.)
Locust
( Robinia
spp.)
perennial/
annual grasses
Reed canary
grass
Phalaris
arundinacea L.
Miscantus (Miscanthus sinensis A.., Miscanthus sacchariflorus M., Misaccantus x giganteus)
Switchgrass
(Panicum
virgatum L.)

## Slide 27
Second generation biofuels
advantages
- Security of supply
- Rustainability
- Reduction of green house gas emissions
- Regional (rural) development
- Social structure & agriculture

## Slide 28
second generation BIOFUELS
advantages
Soil and land
- production on soil not applicable for food (contaminated, brownfields, abandonded…)
- more input of C to soil via root exudates  increased organic C
Air
- Can displace fossil fuels and thus contribute to GHG emissions
reduction
- Biofuels can reduce the emissions of some pollutants from vehicle
exhaust (e.g. fine particles and carbon monoxide)

## Slide 29
second generation BIOFUELS
risks
- similar to risks coming from the first generation if produced in intensive agricultural production systems
- potential risk for biodiversity
To minimaze risks, biomass feedstock should be
- producible with low inputs (fuel, fertilizers, pesticides)
- producible on land with low agricultural value
- conversion of feedstock into biofuels should require low net energy inputs

## Slide 30
Third generation
Algae / cyanobacteria / water plants
H2 production
  some cyanobacteria
Biomass production
  accumulated lipids (up to 70%)  biodiesel
  polysacharadies  fermentation
  biomass  production of biogas
©Varicon Aqua

## Slide 31
Third generation
Advantages
  Energy from sun
  High future potential
  No conflict with food production
  Can grow on waste-water
Disadvantages
  Problematic / costly separation
  Problematic / costly processing
  Wet biomass
  Problematic regulation

## Slide 32
Fourth generation
Experiments only
Photobiofuel cells with cyanobacteria producing H2 + electricity
Isolation of photosynthetic aparatus and its immobilization
Genetically modofied Escherichia coli to produce
  lower molecular aliphatic hydrocarbons
  hydrolyzing enzymes (cellulases)
knock-out CLostridia
  ….

## Slide 33
Biotechnology background

## Slide 34
Ethanol fermentation
Yeast (Saccharomyces cerevisiae…)
Bacteria (Zymomona mobilis)
Anoxic process – in the presence of O2, microbes respirate to CO2 + H2O
Glc  2 C2H5OH + 2 CO2
Different metabolism in yeast and Zymomonas

## Slide 35
Yeast fermentation
1. Standard glycolysis Glc  pyruvate
  yealds 2 ATP of energy + 2 NADPH
2. Decarboxylation pyruvate  CH3CHO+CO2
3. Reduction CH3CHO + NADH  CH3CH2OH + NAD+
O
O
H
O
H
O
H
O
H
C
H
2
O
H

## Slide 36: Zymomonas fermentation
Entner-Doudoroff pathway
  Combination of glycolysis and pentose cycle
  Glc  Glc-6-P
   oxidation to 6-P-glukonolacton
   hydrolysis to 2-keto-3-deoxy-6-fosfogluconate
   dehydratation to 2-keto-3-deoxyfosfoglukonate
   cleavage to glyceraldehyd-3-fosfate + pyruvate
  oxidation of glyceraldehyde to 1,3-bisphosphoglycerate
  dephosphorylation to 3-phosphoglycerate (+1 ATP)
  isomeration to 2-phosphoglycerate
  dehydratation to phosphoenolpyruvate
  dephosphorylation to pyruvate (+1ATP)
  Overall gain of 1 ATP only

## Slide 37: Zymomonas fermentation
Further decarboxylation and reduction to CH3CH2OH
Zymomonas gain only half of the energy compared to yeast  higher ethanole yielads
Zymomonas have also higher ethanol tolerance (>20%)  better processing

## Slide 38: Ethanol fermentation
For fermentation the material must be hydrolyzed to monosaccharides
Easy in case of sugarcane
Moderate in case of starch (wheat…)
  Enzymatic treatment using amylases enzymes
Complicated in case of lignocellulose
  Combination of biotic and abiotic processes
  Usually requires heating

## Slide 39: Biogas
Natural processes carried out by consorcia of microorganisms
  known from ruminants, swamps…
Intensified in biogas stations
www.biocycle.net

## Slide 40: Acetone-butanole fermentation
wikipedia commons

## Slide 41: Clostridium fermentation
Strictly anaerobic process
  Clostridia do not have antioxidation mechanisms  susceptible to oxygen
Tha balance between products can be modified by cultivation conditions and equilibrium shifts

## Slide 42: Perspectives for waste utilization

## Slide 43: Perspectives for waste utilization
Various wastes can be utilized for (bio)fuels
Currently of interest due to implementation of EU strategy of circular economy
Maximal utilization of wastes to resources
  material (recycling)
  energy
Requires separated collection

## Slide 44: Circular economy
EU, MŠMT

## Slide 45: Waste pyramid
landfill
energy
Material recycling
prevention

## Slide 46: Waste pyramid - wider
landfill
incinerate
transform to heat
transform to energy
downcycle
recycle
upcycle
repair
reuse
reduce
refuse

## Slide 47: Thermolysis (pyrolysis)
Thermical decomposition of organic chemicals
Applicable for biomas
Applicable for wastes

## Slide 48: Thermolysis (pyrolysis)

## Slide 49: Thermolysis (pyrolysis)
gas

## Slide 50: Thermolysis (pyrolysis)
gas
oil

## Slide 51: Thermolysis (pyrolysis)
gas
oil
char (biochar)

## Slide 52: Thermolysis (pyrolysis)
Pyrolysis gas is suitable fuel
  for heating
  for running motors (co-generation)
  requires cleaning (PAH contamination)
  positive balance even if used for heating of the process
Pyrolysis oil can be transformed to gasoline / diesel
Requires separated material

## Slide 53: Waste tyres thermolysis
>120 °C, 21 hod
10 tun input
45%-55% oil
 C 30%-35%
 steel 10%-15%
 gas 8%-10%
https://oilpyrolysis.net/equipment/Waste-Tire-Recycle-to-Fuel-Oil-Project.html

## Slide 54: Production of algal biomass using wastewater
Algae are autotrophs and require inorganic sources of C, N, P, S + mikronutrients
These are often present in wastewater to be eliminated
 joint water treatment and biomass production
in ponds or photobioreactors
usually applicable for moderate pollution only
potential of mixotrophic growth  higher lipid content

## Slide 55: Food waste fat to biodiesel
Food waste contains significant proportion of lipids
Potential of proccessing to biodiesel
Unipetrol proposed motivational collection on gas station – discount for fuel for submited waste oils
Helps prevention of canalization clogging

## Slide 56: Pieces from our research – production of Miscnathus x giganteus on marginal and contaminated soils
Valentina Pidlisnyuk, Diana Nebeská, Josef Trögl, Hana Malinská

## Slide 57: Why Miscanthus x giganteus?
Perennial grass
C4 metabolism
Low nutrition demand
Second generation biofuel crop
15-25 t/ha (agricultural soil)
Heat value 17 MJ/kg
Non-invasive

## Slide 58: C4 plants

## Slide 59
Biomass with multiple uses
Cadoux et al, 2013
biofuel
mulch
animal bedding
heat
Miscanthus x giganteus
building materials
packaging

## Slide 60: Project’s Goals:
to enhance environmental security of military sites by developing phytotechnology to produce biomass in large quantities on contaminated lands such that the two goals of biomass production and soil improvement are accomplished effectively and efficiently
to conduct laboratory and field research in order to investigate biomass production as affected by concentrations and nature of contaminants, soil moisture, and nutrients
to study the effect of Miscanthus xgiganteus (second generation energy crop) biomass production on soil quality and microbiology, insect and nematode biodiversity
to test biomass for using as:
a) direct source of energy
b) pellets
SPS MYP G4687: New Phytotechnology for Cleaning Contaminated Military Sites, 2016-2021
military-site-cleaning.cz
Science for peace and security
Notes: The goals of the project are: to avoid environmental damage, to protect the population from negative effects caused by contaminated military sites and to render sites fit for subsequent commercial, recreation and other civilian uses

## Slide 61
Main partners:
Jan Evangelista Purkyne University, Czech Republic
National University of Life and the Environment, Ukraine
Kansas State University and Kansas Agricultural Research Station, USA
Institute of Plant Biology and Biotechnology, IPBB, Kazakhstan
National University “Lvivska Polytechnika”, Ukraine
Team
Liasoning institutions:
University of Zagreb, Croatia
Warminsko-Mazursky University, Poland
Wroclaw University of Life Science
and the Environment, Poland
End-users:
State Committee of Energy Saving, Ukraine
Slovakian Environmental Agency, Slovakia
Kamenetz-Podilsky city council, Ukraine
Dolyna city counsil, Ukraine
Environmental Division, Fort-Riley, USA
“Ecology Engineering”, Kazakhstan

## Slide 62: Background
Phytoremediation
decontamination of soil
Biomass
clean biomass for further processing (energy, biobased products)
Phytoextraction
62
Notes: Různé cíle při fytoremediaci a při produkci biomasy  potřeba kytka, co zvládne oboje při jednom

## Slide 63: Aims
1) Plant – contamination
2) Plant – soil microorganisms
3) Biomass improvement

## Slide 64: Lab research on M.x giganteus resistance, metal(loids)-contaminated military soils*,**
Kamenetz-Podilsky (Ukraine)-former military storage and Sliac (Slovak Republic) - former airports of the SU. Both are contaminated by metal)loid)s
High adaptability of M.x giganteus for growth at the metal-contaminated military soils (Ti,Mn,Cu,Zn,Sr, As,Pb and Zr).
Accumulation of metals predominantly in roots
Accumulation in above-ground parts significantly lower (Fe, Ti, Mn, Cu, Zn, Sr) or comparable to zero (As, Pb and Zr)
Shoot/root coefficients significantly lower than 1  absence of metals hyper-accumulation in the plant
*Pidilsnyuk V., Trogl J., Stefanovska T., Shapoval P., Erickson L. 2016. Preliminary results on growing second generation biofuel crop Miscanthusxgiganteus at the polluted military site in Ukraine. Nova Biotechnologica et Chimica: 15 (1): 77-84.
**Pidlisnyuk V., Erickson L., Trogl J., Shapoval P., Davis L., Popelka J. Stefanovka T., Hettiarachchi G. 2018. Metals uptake behaviour in Miscanthus x giganteus plant during growth at the contaminated soil from the military site in Sliač, Slovakia Polish J. Chem. Technol., 20(2): 1-7.

## Slide 65
Dynamic of foliar metal(loid) concentration in M.xgiganteus leaves during vegetation at Sliac soil
Pidlisnyuk V., Erickson L., Stefanovska T., Popelka J., Hettiarachchi G., Davis L., Trögl J.: Potential phytomanagement of military polluted sites and biomass production using biofuel crop Miscanthus x giganteus. Env. Pollut. 249 (2019) 330-337.

## Slide 66: Mimoň military airoport
Metals + petroleum
Cd
Pb
Zn
Cu
Cd
Pb
Zn
Cu
Cd
Pb
Zn
Cu
Notes: Prezentováno loni na závěrečném semináři; první pokus, výsledky z něj podklad pro design dalších experimentů

## Slide 67: Biomass
Chart: Biomass [g]
| Control | Military site | MIX 3:1 | MIX 1:1
2016 | 167.61 | 116.52 | 3.11 | 0
2017 | 213.9 | 181.2 | 5.9 | 6.5
Notes: Military nižší než kontrola ale pořád OK, s ropou přežije ale výnos zanedbatelný

## Slide 68: Physiological parameters
Notes: Potvrzení, že v ropě kytky strádají pomocí fluorimetru

## Slide 69: Petroleum hydrocarbons
Chart: C10-C40
| Control | Military site | MIX 3:1 | MIX 1:1
5/16 | 0 | 0 | 8642 | 21290
11/16 | 0 | 0 | 6854
12/17 | 0 | 0 | 5155 | 13520
Preventive value according to Decree n. 153/2016 Sb.
Notes: Degradace probíhá (autochtonní mikroorganismy), proto pravděpodobně v druhém roce už kytka žije

## Slide 70: Soil microorganisms - stress
D. Nebeská, H. Malinská, J. Trögl, V. Pidlisnyuk, J. Popelka, P. Kuráň, A. Medžová, M. Smaha. Growing Miscanthus x giganteus in post-military soil and soils contaminated by petroleum hydrocarbons: remediation and biomass production (in prep.)
Notes: V control + military stres postupně klesá k nule; v kontaminované, kde kytka moc neroste, postupně narůstá

## Slide 71: Limit for Mxg AH tolerance
Contaminated soil from previous experiment + military soil
+
+
+
1:0 2:1 1:1 1:2 0:1
1 2 3 4 5
Notes: Navazující pokus na předchozí, další zředění pomocí půdy z letiště

## Slide 72: Limit for Mxg AH tolerance
Chart: Inhibition of biomass production
| 0 | 0 | 0 | 1404.2412046092734 | 1404.2412046092734 | 1404.2412046092734 | 1571.7681067291273 | 1571.7681067291273 | 1571.7681067291273 | 2187.5737470841414 | 2187.5737470841414 | 2187.5737470841414 | 3625.1810545856051 | 3625.1810545856051 | 3625.1810545856051
Plant height | 0.090909 | -0.033058 | -0.057851 | 0.29752 | 0.36364 | 0.47934 | 0.78512 | 0.69421 | 0.79339 | 0.83471 | 0.90083 | 0.89256 | 0.78512 | 0.78512 | 0.77686
Biomass | 0.029699 | 0.071277 | -0.10098 | 0.83369 | 0.80017 | 0.7412 | 0.97051 | 0.96882 | 0.92597 | 0.97539 | 0.97136 | 0.9877 | 0.97624 | 0.96818 | 0.98176
Notes: Všechny přežily, ale od 1500 mg/kg už velmi málo biomasy, i předchozí varianty výrazně nižší než kontrola

## Slide 73: Effect of Mxg on soil microorganisms
NATO experiment in Banská Bystrice
2 years pot experiment
Soil from post-military airport Sliač
Metals and metalloids: As, Cu, Fe, Mn, Sr, Ti, Zn, Zr

## Slide 74: Effect of Mxg on SM with metals
Nebeská D., Trögl J., Pidlisnyuk V., Popelka J., Veronesi-dáňová P., Usťak S., Honzík R.: Effect of growing Miscanthus x giganteus on soil microbial communities in post-military soil. Sustainability 10(11) (2018) 4021.

## Slide 75: Effect of Mxg on SM in marginal sites (field)
Hradčany 1
Hradčany 2
Chomutov
Všebořice

## Slide 76: Effect of Mxg on SM in marginal sites (field)
Comparison od rhizosphere soil, bulk soil, field soil between plants and soil out of field
Notes: Na podzim odebrané vzorky

## Slide 77: Effect of Mxg on SM in marginal sites (field)
In process
Notes: Máme první výsledky (poster Polsko), ale ještě budou fosfolipidy. Zatím se zdá, že větší vliv na polích bez konkurence plevelů a ve velmi chudé půdě.

## Slide 78: PGRs treatment
1 yeat pot experiments with soil from post-military sites (Hradčany CZ – airport and Dolyna UA – tank training area)
Different PGRs application

## Slide 79: Acknowledgement

## Slide 80: Case-study: Biofuel in Brazil
Brazil is the world's second largest producer of ethanol fuel , and until 2010, the world's largest exporter. Brazil and the US lead the industrial production of ethanol fuel, accounting together for 87.8 percent of the world's production in 2010, and 87.1 percent in 2011.
In 2011 Brazil produced 21.1 billion liters , representing 24.9 percent of the world's total ethanol used as fuel.[
Brazil is considered to have the world's first sustainable biofuels economy and the biofuel industry leader, a policy model for other countries; and its sugarcane ethanol "the most successful alternative fuel to date.”
However, some authors consider that the successful Brazilian ethanol model is sustainable only in Brazil due to its advanced agri-industrial technology and its enormous amount of arable land available

## Slide 81
Brazil’s 37-year-old ethanol fuel program is based on the most efficient agricultural technology for sugarcane cultivation in the world, uses modern equipment and cheap sugar cane as feedstock, the residual cane-waste is used to produce heat and power, which results in a very competitive price and in a high energy balance (output energy/input energy), which varies from 8.3 for average conditions to 10.2 for best practice production
In 2010, the US EPA designated Brazilian sugarcane ethanol as an advanced biofuel due to its 61% reduction of total life cycle greenhouse gas emissions

## Slide 82: Environmental argument in favor of ethanol
Unlike petrol, it is free of pollutants such as sulphur dioxide, while the carbon dioxide emissions it produces can be cancelled out by growing another sugar-cane plant
And in one lasting benefit, ethanol had already replaced lead in conventional Brazilian petrol, putting paid to the worst kind of airborne pollution
A new generation of alcohol-powered cars entered production in Brazil in 2003, after the government decided that cars capable of burning ethanol should be taxed at 14%, instead of 16% for their exclusively petrol-powered counterparts

## Slide 83: “Flex-fuel" cars
Unlike earlier models, these are "flex-fuel" cars - equally happy with pure alcohol, pure petrol, or any blend of the two
When the fuel tank is filled, a special computer chip analyses the mixture and adjusts the motor according to how much ethanol and how much petrol it contains
In 2004, the first full year that "flex-fuel" cars were on sale, they accounted for more than 17% of the Brazilian market
In 2010, they scored an even bigger success, overtaking petrol-driven models for the first time since the 1980s and taking 53.6% of the market for new cars

## Slide 84: Background: Brazil's state-run alcohol fuel programmer
Was set up for patriotic, not financial or environmental reasons
The military government (ran the country in 1964 -1985) wanted to reduce dependence on Middle Eastern petroleum during the 1970s oil crisis
The technology was far from new, having been around since the 1920s, but no country had employed it on such a scale
Under the Pro-Alcohol programmer, farmers were paid generous subsidies to grow sugar-cane, from which ethanol was produced
The price at the pump was also subsidized to make the new fuel cheaper than petrol, while the motor industry turned out increasing numbers of vehicles adapted to burn pure ethanol
As a result, in 1985 and 1986, more than 75% of all motor vehicles produced in Brazil - and more than 90% of cars - were designed for alcohol consumption

## Slide 85: Promotion of using biofuel in Brazil
There are no longer any light vehicles in Brazil running on pure gasoline
Since 1976 the government made it mandatory to blend anhydrous ethanol with gasoline, fluctuating between 10% to 22% and requiring just a minor adjustment on regular gasoline engines
In 1993 the mandatory blend was fixed by law at 22% anhydrous ethanol (E22) by volume in the entire country, but with leeway to the Executive to set different percentages of ethanol within pre-established boundaries
In 2003 these limits were set at a minimum of 20% and a maximum of 25%
Since 2007 the mandatory blend is 25% of anhydrous ethanol and 75% gasoline. The lower limit was reduced to 18% in 2011 due to recurring ethanol supply shortages and high prices that take place between harvest seasons

## Slide 86: Sugar cane
Giant, thick, perennial grass cultivated in tropical and subtropical regions worldwide for its sweet sap, a major source of sugar and molasses. The plant grows in clumps of solid stalks with regularly spaced nodes or joints, each with a bud that can be planted for commercial asexual propagation.
Mature canes may be 36 m tall and 2.5-7.5 cm in diameter. Molasses, the syrup remaining after sugar is crystallized out of the juice, is used in cooking, in making rum, and as feed for farm animals.
Residual cane fiber (bagasse) is burned as fuel or used as filler for paper and particleboard.

## Slide 87
Case-study:
Warmia@Mazury

## Slide 88: Renewables in Warmia andMazury –the state of the art
the share of energy from renewablesintotalusage, 3.1%
big electric power stationsarelocated outside the region (Gdańsk, Ostrołeka, Włocławek)and electricity is powered mainly by fossil fuels
installed capacity of electric power in the region –90 MW
heating plants–83%
hydropower plants–15%
other renewables–2%
heating energy is supplied by 605 local boiler houses with transmission grid 503 km and supplied heat of 9800 TJ

## Slide 100: Future outlook
Combined environmental issues
  cultivation of algae on wastewater
  production of biomass + bioremediation
  use of wastes

## Slide 101: Renewable energy: Biofuels Overviews and case-studies

## Slide 102: Benefits expected
Economic benefits
new sources of energy – energy independence
Social benefits
new jobs
Ecological benefits
Decreasing emission of pollutants
possibilities for rural areas
better quality of life
Combat the climate change

## Slide 103: Impact of biofuels on sustainable development*
  Economic impact
A positive effect is investment in the development of transport, agriculture and reduced import related to increased energy security.
Innovation and technological development may be stimulated, leading to long-term benefits for the economy.
A negative aspect is the higher costs of production compared to traditional fuels, the need for subsidies, elimination of subsidies for leaving land without crop as well as more expensive energy and fuel.
  Social impact
New jobs are created. Environmental awareness in society may increase.
Unemployment may increase due to higher costs of production. The poor may be hit by higher energy and food prices,
  Environmental inpact
There are no visible advantages. The research discussed shows that reduction in the emission of greenhouse gasses is unlikely. It may even be that these emissions increase! The reduced areal without crop is likely to create different types of negative environmental effects.
*Zabochnicka-Swiątek. M., Sławik. L., Wady i zalety biopaliw na przykładzie bioetanolu, http://www.plan-rozwoju.pcz.pl/dokumenty/konferencja/artykuly/27.pdf;

## Slide 104
World biofuel production in 2008, and trends
BIOFUELS
WORLD production
Country | Ethanol in Mn liters in 2008 | Ethanol in % change 2005-2008 | Biodiesel in Mn liters in 2008 | Biodiesel in % change 2005-2008 | Total in Mn liters in 2008 | Total in % change 2005-2008
Brazil | 22 239 | 46 | 1 089 | - | 23 328 | 53
Canada | 1 083 | 167 | 205 | 388 | 1 288 | 188
China | 3 964 | 15 | 114 | - | 3 964 | 15
USA | 34 463 | 125 | 2 709 | 266 | 37 172 | 131
EU | 5 022 | 71 | 8 064 | 123 | 13 086 | 100
World | 70 636 | 78 | 15 140 | 230 | 85 776 | 93
Source: EU, 2010

## Slide 105: Conversion of agricultural feedstocks into liquid biofuels

## Slide 106: Biofuels in the EU : pieces of legislation
EU Strategy for Biofuels COM(2006)
EC Communication on the share of renewable energy in the EU, COM(2004) 366 final
Directives: 2001/77/EC on renewable energy resources, 2003/30/EC on the use of biofuels or other renewable energy sources in transport, 2009/28/EC and 2004/8/EC on the promotion of cogeneration of heat and electricity
SEC(2011) 130 final - Recent progress in developing renewable energy sources and technical evaluation of the use of biofuels and other renewable fuels in transport in accordance with Article 3 of Directive 2001/77/EC and Article 4(2) of Directive 2003/30/EC
Biofuels in the EU a vision for 2030 an beyond (2006)
Biofuels in the European context: Facts and Uncertainties (2008)

## Slide 107: Can biofuels help mitigate climate change?
Bioenergy crops can reduce or offset greenhouse gas emissions
These crops generate co-products such as protein for animal feed, thus saving on energy that would have been used to make feed by other means.
Some crops can generate more greenhouse gases than
do fossil fuels
Maize can generate green house gas savin of about
1.8 tonnes of carbon dioxide per hectare per year, and switchgrass can generate savings of 8.6 tonnes per hectare per year, (Fargione et al., 2008; The Royal Society, 2008; Searchinger, 2008).

## Slide 108: CO2 abatement Benefits From Growing Perennial Grasses in Place of Annual Cropping and Permanent Grassland Over 7 Years (in t ha-1)
 | PRG in place of arable cropping |  | PRG in place of grassland | 
 |  | CO2 |  | CO2
 |  | removed |  | removed
 |  | from the |  | from the
 |  | atmosphere |  | atmosphere
Miscanthus |  | 208.89 |  | 35.89
RCG |  | 187.28 |  | 10.28
Switchgrass |  | 180.18 |  | (1.82)
Source: Bullard and Metcalfe, 2001